## Slide 1: SHIP LOADS AND STRESSES
GROUP B:
Bhullar Kunwar Puneet Singh
Krishnan Prashant
Kulhari Sundeep
Mahadik Rohan

## Slide 2: With the aid of diagrams, describe the various types of deformations in ship structures due to external forces and classify them as due to Static or Dynamic forces.

## Slide 3: The ship at sea or lying in still water is constantly being subjected to a wide variety of stresses and strains, which result from the action of forces from outside and within the ship. These forces may initially be classified into STATIC FORCES DYNAMIC FORCES

## Slide 4: STATIC FORCES
These are due to
Internal forces resulting from structural weight, cargo and machinery weight.
External static forces including the hydrostatic pressure of the water on the hull.

## Slide 5: DYNAMIC FORCES
They result from
The ship’s motion at sea.
The action of wind and waves.
The effects of operating machinery.

## Slide 6: DEGREES OF FREEDOM
A ship is free to move about six degrees of freedom.
Three linear and three rotational.
Various forces acting on ship are constantly varying in degree and frequency.
This movement of the ship introduces dynamic forces which result in stresses on the ship’s structure.

## Slide 7: HOGGING
Wave crest at mid-ships, buoyancy in this region is increased.
Wave trough at the ends of the ship, buoyancy is reduced.
This loading condition will result in a significantly increased bending moment.
This causes the ship to hog.
Extreme condition giving maximum bending moment in a ship’s structure.
This is a result of Dynamic forces.

## Slide 8: SAGGING
Wave trough at mid-ships, buoyancy in this region is reduced.
Wave crest at the ends of ship, buoyancy is increased.
This loading condition will result in a significantly increased bending moment.
This causes the ship to sag.
This is a result of Dynamic forces.

## Slide 9: RACKING
When a ship rolls, it results in forces tending to distort it transversely.
This may cause deformation at corners.
Deck tends to move laterally relative to bottom structure.
Shell on one side tends to move vertically relative to other side.
This is termed racking.
Greatest effect felt when ship is in light or ballast condition.
This is a result of Dynamic forces.

## Slide 10: TORSION
When a ship is subjected to a twisting moment, it is said to be in Torsion.
Ship heading obliquely(45 degrees) to a wave will be subjected to righting moments of opposite direction at its ends.
This tends to twist the hull putting it in Torsion.
This is a result of Dynamic forces.

## Slide 11: STRESSES DUE TO WATER PRESSURE
Water pressure increases with depth and tends to set in the ship’s plating below the water line.
Transverse section of a ship is subjected to static pressure from the surrounding water.
Considerable distortion of structure can occur in absence of adequate stiffening.
This is a result of Static forces.

## Slide 12: STRESSES DUE TO DRY-DOCKING
Tends to set the keel upwards.
Due to the up-thrust of the keel blocks.
Tendency for the ship’s sides to bulge outwards.
Bilges tend to sag.
This is a result of Static forces.

## Slide 13: SLAMMING OR POUNDING
While heaving or pitching, the forward end leaves and re-enters the water with a slamming effect.
Flat areas of plating are brought into violent contact with water at a very acute angle.
There is a loud bang and the ship shudders.
Momentum of the ship receives a check and energy is imparted to the ship girder to make it vibrate.
This is also known as pounding and is a result of Dynamic forces.

## Slide 14: SLAMMING

## Slide 15: SLAMMING OR POUNDING

## Slide 16: PANTING
Movement of waves along a ship causes fluctuations in water pressure on the plating.
This tends to create an in-and-out movement of the shell plating, known as panting.
Effect is particularly evident at the bows as the ship pushes its way through the water.
Pitching motion of the ship produces additional variations in water pressure, particularly at the bow and stern, which also causes panting of the plating.