## Slide 1: HULL FRAMING SYSTEMS
by
GROUP-E
MEMBERS
1 JUDE RINALDO
2 AARYL D’SA
3 SWAROOP SUNDER
4 JUDE PRADEEP

## Slide 2
Describe with neat diagrams the longitudinal framing system and list their advantages and disadvantages.

## Slide 3: FRAMING
The shell(bottom and side)and deck plating of the ship has to be stiffened internally to prevent it from collapsing. The stiffening is generally provided by:
Primary supporting members
Secondary supporting members
Primary supporting members are the big members or metaphorically speaking the big bones such as web frames,girders,solid floors,etc
Secondary supporting members are the small bones of the ship such as longitudinals,hold frames,deck beams.

## Slide 4: Longitudinal framing system
Longitudinal framing system is included in secondary supporting members
Longitudinal framing system is used for larger ships where longitudinal strength is a major consideration
They are much smaller in size as compared to primary supporting members

## Slide 5
Longitudinal framing system

## Slide 6
Starting from the keel to the deck:
Keel
- Large center-plane girder
- Runs longitudinally along the bottom of the ship
Longitudinals
- Girders running parallel to the keel along the bottom
- It provides longitudinal strength
Longitudinal Structural Components

## Slide 7
Stringer
Girders running along the sides of the ship
Typically smaller than a longitudinal
Provides longitudinal strength
Longitudinal Structural Components
Deck Girder
Longitudinal member of the deck frame (deck longitudinal)
….Primary role of longitudinal members :
Resist the longitudinal bending stress due to sagging and hogging

## Slide 8
LONGITUDINAL
MEMBERS
TRANSVERSE
MEMBERS
FLOOR
LONGITUDINAL
DECK BEAM
FRAME
STRINGERS
DECK
GIRDERS
DECK PLATING
PLATING
KEEL

## Slide 9: Longitudinal framing system
In this system,all the secondary supporting members are fitted in the longitudinal direction and are known as longitudinals.
Some of them are:
Bottom longitudinals
Side longitudinals
Deck longitudinals
The system consist of many small,closely spaced longitudinals supporting the plating directly and being supported in turn by a few large ,widely spaced longitudinals

## Slide 10: Longitudinal framing system
The bottom longitudinal on centreline,or centre girder, is extra large and heavy,principally to carry the loads imposed by keel blocks during dry docking
Very deep, heavy transverse structures called transverse webs or web frames are constructed at intervals of about 3 to 5 metres to support the longitudinals
Where a ship’s length exceeds 120 m it is considered desirable to adopt longitudinal framing
Tankers greater than 200 m in length must be framed longitudinally

## Slide 11: Longitudinal framing system

## Slide 12
Longitudinal framing system

## Slide 13: Longitudinal framing system in Tankers
When a ship exceeds 120 m it is considered desirable to adopt longitudinal framing
This is the main system used in tankers greater than about 200m in length where longitudinal strength is a major consideration
Adoption of any other system will result in unacceptably large hull weight
Longitudinal stiffeners spaced about 600 to 900 mm apart give direct support to the plating of the decks,sides,bottom and bulkheads
They also contribute to the longitudinal strength of the ship,making the longitudinal framing system more structurally efficient than the transverse system

## Slide 14
Longitudinal framing system in Tankers

## Slide 15
Longitudinal framing system in Tankers

## Slide 16: Advantages of longitudinal framing system
The advantages of longitudinal framing system are as follows:
Longitudinally stiffened plating is more resistant to buckling especially prevalent in ship’s upper deck.
When the deck or bottom is subjected to compressive stresses as it bends in a seaway than it would be if stiffened transversely.
Longitudinal stiffeners supporting side shell and bulkhead plating are subjected to variable pressures from the sea or from liquid cargo. The hydrostatic pressure on each successive longitudinal and its associated plating increases with its depth below the waterline or below the surface of the liquid in the tank.

## Slide 17
Each longitudinal can be sized to withstand the maximum pressure associated with its depth in the ship, thus achieving an efficient use of structural material.
Graduated size cannot be done effectively with transverse frames, which as a result are only heavy at their upper ends.
Advantages of longitudinal framing system

## Slide 18: Disadvantages of longitudinal framing system
Though the longitudinal framing system has a lot of advantages,it also has some disadvantages.They are as follows:
The intrusion of deep webs into prime cargo spaces for ships carrying packaged cargo is an disadvantage.
Difficulty arises in the structural arrangements near the ends of the ship.
As the hull narrows towards the bow and stem,however, the girth necessarily reduces and the longitudinals becomes closer together
Difficulties in construction arise when they converge so closely that some longitudinals have to be eliminated