## Slide 1: HULL FRAMING SYSTEMS
GROUP B :
SUNDEEP KULHARI
PRASHANT KRISHNAN
PUNEET BHULLAR
ROHAN MAHADIK

## Slide 2: QUESTION
DESCRIBE THE DIFFERENT TYPES OF PRIMARY AND SECONDARY SUPPORTING MEMBERS?

## Slide 3: PRIMARY SUPPORTING MEMBERS
They are the big members or metaphorically speaking the big bones such as web frames, girders, solid (i.e. plate) floors, etc.
They consist of :
Transverse Rings
Longitudinal girder

## Slide 4: TRANSVERSE RINGS
They are fitted along the length of the ship at about intervals of 3 – 4 meters apart and can be divided into three parts :
Bottom transverse
Web frame
Deck transverse

## Slide 5: BOTTOM TRANSVERSE
It is the first part at the bottom of the ship.
It is represented by a solid floor in ships with a double bottom construction.
Its height is similar to that of a centerline girder.

## Slide 6: WEB FRAMES
It is the second part on the side of the ship.
Its depth is about 0.125 times the vertical distance from the tank top to the deck above.
These are fitted at about every five frame spaces.

## Slide 7: DECK TRANSVERSE
It is the third part n the deck.
Its depth varies dependent upon the span between supporting girders or bulkheads , or between girders and side frames.

## Slide 8: LONGITUDINAL GIRDERS
Fitted at the bottom, deck and on the ship side.
On the bottom and deck of a ship centerline and side girders are fitted.
On the ship side, horizontal girders known as side stringers (or stringers) are fitted.
The number of side stringers depends on the depth of the ship.

## Slide 9: SECONDARY SUPPORTING MEMBERS
They are much smaller in size as compared to the primary supporting members. Manufactured sections of bulb plates or unequal angles are normally used for those secondary supporting members. They are fitted usually at spacing of less 1000 mm apart.

## Slide 10
Transverse Framing System
Longitudinal Framing System
Combined or Mixed Framing System
There are three possible ways to fit the
secondary supporting members:
CONTD………

## Slide 11: TRANSVERSE FRAMING SYSTEM
The hold frames are fitted transversely
Longitudinal deck girders support the transverse deck beams
Longitudinal strength in a transversely framed ship is provided by:
  The centre girder, the shell plating and inner bottom plating
  By the deck plating outboard of hatch and machinery casing openings
  By a number of large, widely spaced longitudinal members e.g. longitudinal deck girders

## Slide 12: TRANSVERSE FRAMED OIL TANKER

## Slide 13: LONGITUDINAL FRAMING SYSTEM
All secondary supporting members are fitted the longitudinal direction and are known as longitudinals
The system consists of many small, closely spaced longitudinals supporting the plating directly and being supported in turn by a few largely spaced longitudinals
It is in tankers that this system in its purest form is employed
They also contribute to the longitudinal strength of the ship, making the longitudinal framing system more structurally efficient than the transverse system

## Slide 14: LONGITUDINALLY FRAMED OIL TANKER

## Slide 15: COMBINED FRAMING SYSTEM
A combination of both transverse and longitudinal framing is adopted in the same cross section of the ship.
Longitudinal framing is used in the bottom and decks.
This has the advantage of extra longitudinal strength and resistance to compressive plate buckling.
Transverse framing is used in the sides.
This precludes the need for deep webs that might inhibit efficient cargo stowage.

## Slide 16: COMPOSITELY FRAMED OIL TANKER