## Slide 1: Hull Framing Systems
Made by:
Vishwas Tomar
Nihar Herwadkar
Md. Arif Khan
S. Krishnanandh

## Slide 2: Compare the advantages and disadvantages of longitudinal and transverse framing system.

## Slide 3: What is framing?
The shell of a ship consists of bottom, side and deck plating. These are stiffened (supported) internally to prevent it from collapsing. This supporting arrangement is called framing.
Framing consists of –
1. Primary supporting members, and
2. Secondary supporting members.

## Slide 4
Some properties of secondary supporting members are:
Much smaller in size as compared to primary supporting members
Manufactured sections of bulb plates or unequal angles are used
Fitted usually at spacing of less than 1000 mm apart

## Slide 5
Here we will be comparing:
transverse framing system and
longitudinal framing system
which falls under the category of secondary supporting members.

## Slide 6
In a Transverse framing system:
Hold frames are fitted transversely.
Bottom member named as open floor, side member as hold frame and deck member as deck beam respectively.

## Slide 7
In a longitudinal framing system:
All secondary supporting members are fitted in longitudinal direction.
These are known as longitudinals (bottom, side and deck respectively)

## Slide 8: Comparisons between the two systems:

## Slide 9
Transverse system
Transverse framing were structurally sound and satisfactory in service.
But most of the transverse stiffeners contribute nothing to ship’s resistance of longitudinal bending.
Therefore it was not optimal for structural efficiency i.e. achieving required strength for least weight.

## Slide 10
Longitudinal system
The longitudinal system has superior structural efficiency.
Longitudinal system support shell plating against local loading caused by water pressure and cargo loads (which transverse frames also do)
They contribute to ship’s resistance of longitudinal bending (which transverse frames do not)

## Slide 11: Advantages of longitudinal framing system over the transverse framing system:
More resistant to buckling between longitudinal stiffeners when deck or bottom is subjected to compressive stresses.
As hydrostatic pressure on a longitudinal and associated plating increase with depth below the waterline or below the surface of liquid in the tank, each longitudinal can be sized to withstand the maximum pressure associated with its depth. Thus achieving an efficient use of structural material.

## Slide 12: Disadvantages of longitudinal framing system over transverse framing system:
The deep webs intrude into prime cargo spaces for ships carrying packaged cargo.
As hull narrows towards the bow and stem, the longitudinals become closer together. Thus some of them have to be eliminated when they converge too closely. This results in difficulties in construction.