## Slide 1: HULL FRAMING SYSTEMS
GROUP C
DMS(DO)

## Slide 2: QUESTION
Describe and compare transverse and longitudinal framing systems and explain the need for combination framing system.

## Slide 3: FRAMING SYSTEMS
There are three possible ways to fit the secondary supporting members:
Transverse Framing System
Longitudinal Framing System
Combined or Mixed Framing System

## Slide 4: TRANSVERSE FRAMING SYSTEM
The hold frames are fitted transversely
Longitudinal deck girders support the transverse deck beams
Longitudinal strength in a transversely framed ship is provided by:
  The centre girder, the shell plating and inner bottom plating
  By the deck plating outboard of hatch and machinery casing openings
  By a number of large, widely spaced longitudinal members e.g. longitudinal deck girders

## Slide 5: TRANSVERSE FRAMED OIL TANKER

## Slide 6: LONGITUDINAL FRAMING SYSTEM
All secondary supporting members are fitted the longitudinal direction and are known as longitudinals
The system consists of many small, closely spaced longitudinals supporting the plating directly and being supported in turn by a few largely spaced longitudinals
It is in tankers that this system in its purest form is employed
They also contribute to the longitudinal strength of the ship, making the longitudinal framing system more structurally efficient than the transverse system

## Slide 7: LONGITUDINALLY FRAMED OIL TANKER

## Slide 8: COMPARISON
No contribution to the ship’s resistance to longitudinal bending.
Not optimal from the standpoint of structural efficiency, i.e. achieving the required strength for the least weight.
More resistant to buckling between longitudinal stiffeners when subjected to compressive stresses while bending in seaway.
Superior structural efficiency because most of the plating stiffeners are in the fore and aft direction.
The intrusion of deep webs into prime cargo spaces for ships carrying packaged cargo is a disadvantage of longitudinal framing system.
As the hull narrows toward bow and stem, the girth necessary reduces.
Difficulties in construction arise when the longitudinal frames converge so closely.
For this reason, transverse framing is usually resorted to at the bow and stem of longitudinally framed ships.

## Slide 9: COMBINED FRAMING SYSTEM
A combination of both transverse and longitudinal framing is adopted in the same cross section of the ship.
Longitudinal framing is used in the bottom and decks.
This has the advantage of extra longitudinal strength and resistance to compressive plate buckling.
Transverse framing is used in the sides.
This precludes the need for deep webs that might inhibit efficient cargo stowage.

## Slide 10: COMPOSITELY FRAMED OIL TANKER

## Slide 11: REFERENCES
Ship Powering and Construction Notes
Naval Architecture Lectures on the web
  http://web.nps.navy.mil/~me/tsse/NavArchWeb/lectures.htm/