## Slide 1: HULL FRAMING SYSTEMS
GROUP D
TARANG VALECHA
APURVA MALI
DHANANJAY R
PRATEEK SINGH

## Slide 2: With the help of diagrams, list the supporting members of the hull frames.

## Slide 3: FRAMING:
The hull must have a framing system to support it because the hull itself, like a bridge, spans a fluid substance.
Whereas a bridge spans air, a hull spans water, and while water is more dense, it is still a fluid and offers lesser means of support than solid ground.
Unless the hull has an adequate system of framing and girders to span the unsupported sections, like a bridge it will buckle and collapse.
Frames serve the purpose of stiffening panels between bulkheads and stringers. Obviously, if a panel is flexing too much, additional framing would prevent that condition.
Some builders scrimp on frames because frames create additional detail work and adds more to labor cost. But since frames are an integral part of ship building they must be given utmost importance

## Slide 4: FRAMES

## Slide 5
FRAMING
Primary supporting
members
Secondary supporting
members
Transverse rings
Longitudinal girders
Bottom transverse
Web frames
Deck transverse
Longitudinals
Hold frames
Deck beams etc

## Slide 6: Supporting members of the framing system:
The stiffening is generally provided by :
PRIMARY and SECONDARY supporting members.

## Slide 7: STERN PLATING
LONGITUDINALS

## Slide 8: BOTTOM TRANSVERSE: The first part at the bottom Is known as Bottom transverse and is represented by a solid floor with double bottom construction. The height of the bottom transverse is similar to that of the centreline girder. WEB FRAME: The second part on the side is known as web frame. The depth of the side web frame is about 0.125 times the vertical distance from the tank top to the deck above ,eg if this vertical line is 10 mts ,the depth of the web wil be 1.25 mts. DECK TRANSVERSE: The third part on the deck is known as deck transverse. The depth of this varies dependant on the span between the supporting girders or bulkheads,or between girder and side frame
Transverse Rings

## Slide 9: STRUCTURAL MEMBERS

## Slide 10: LONGITUDINALS: All the secondary supporting members that are fitted in the longitudinal direction are known as ‘Longitudinals’. HOLD FRAMES: In the transverse framing system,the hold frames are fitted transversely. The side members are known as the hold frame or main frame. DECK BEAMS: In the transverse framing system,the deck member is known as the deck beam. Longitudinal deck girders support the transverse deck beams.
Secondary supporting members