## Slide 1: SHELL CONSTRUCTION
GROUP C
DMS(DO)

## Slide 2: OBJECTIVE
Variations in the thickness of shell plating

## Slide 3: SHELL PLATING
External skin of ship.
Consists of bottom shell plating and the side shell plating.
  Acts as a watertight skin
  Contributes significantly to longitudinal strength.

## Slide 4: BOTTOM SHELL PLATING
Bottom plating refers to the plating from the keel to the turn of the bilge.
This has the greatest thickness because bending stresses is greatest as the plates are located farthest from the neutral axis of the ship.

## Slide 5: STRAKE
Wide strip of longitudinal plating parallel to the keel plating.
Of uniform thickness at the parallel middle body region but tapering towards the ends of the vessel.

## Slide 6: SIDE SHELL PLATING
Refers to the vertical plating from the upper turn of bilge to the weather deck.
The upper strake of the plating adjacent to the strength deck is known as the sheer strake.
As the sheer strake is located at a great distance from the neutral axis, it has greater thickness than other strakes.

## Slide 7: SIDE SHELL PLATING
Where the spacing of stiffening members on shell plating is remarkably different from the spacing, actual spaces is to be used in calculating the thickness of shell plating.

## Slide 8: SIDE SHELL WITH TRANSVERSE FRAMING

## Slide 9: SIDE AND BILGE STRUCTURE

## Slide 10: CLASSIFICATION SOCIETY REQUIREMENTS
Thickness calculation of bottom plates be based on lateral pressure and longitudinal buckling strength of plate.
Heavy shell plating are fitted in way of attachments to stern frame for heel and boss plates in way of spectacle bossing as these areas are subjected to heavy stresses.